## Slide 1: OpenWifi SD card Function

## Slide 2: Write file to SD card
Command: ./side_ch_ctl s g
The file would be saved in:
  /openwifi/save_raw_data_to_sd_card.bin
Modify the filename saved in SD card:
  Change the filename in line 311 of /openwifi/side_ch_ctl.c
    fp_bin = fopen("./save_raw_data_to_sd_card.bin","wb");
  Compile the updated file: gcc –o side_ch_ctl side_ch_ctl.c

## Slide 3: Parsing Infomation
Copy the binary file (save_raw_data_to_sd_card.bin) to PC
Run the script: load_sd_bin.py
The parsed information is saved in .mat file
File size after 1-hour scanning:
  Bin file: 162 MB
  Mat file: 136 MB

## Slide 4: Switch Between 5G/2G Channels
A script is written: /openwifi/set_band.sh
Usage:
  Move to openwifi directory
  ./set band.sh 5 && ./wgd.sh ------> (Only scan 5G channels)
    ./set band.sh 2 && ./wgd.sh ------> (Only scan 2G channels)
    ./set band.sh && ./wgd.sh ------> (Support all channels)